## Slide 1: DIY: Mood Ring Project
A TI-Innovator STEM Project
for the TI-84 Plus CE and
TI-Nspire CX
Notes: This project is considered the entry point for the STEM Projects using TI-Innovator Technology. It is strongly suggested that if your students do not have much familiarity with the coding on the TI calculator, they start with this project to build skills and their confidence, and then progress to more complex projects like the Pet Car Alarm, and/or Smart Water projects.
Note that the default path (active slides) are geared towards TI-84 Plus CE users, but TI-Nspire CX versions of the sample code are hidden, and be unhidden to provide support for students using TI-Nspire CX handhelds. Also note that there are some hidden slides labelled ‘Fast Track’- this is an alternative path you may choose, if students are already comfortable with coding basics, and do not need the step-by-step nature of the 10 Minutes of Code Lessons. It is recommended that the 10 Minutes of Code path is best for students who are new to coding, and/or you have a mixed room of ability levels, as this will help ensure students have similar proficiencies moving forward.

## Slide 2: Overview of Sections:
1. Project Overview and Intro to Programming
Overview
2. Introduction to the TI-Innovator Hub
Classroom Presentation
3. Input and Output
Exploring Sensors:
Supply List
Classroom Presentation
Temp Sensor
Brightness
4. Putting it all together: DIY Mood Ring
Students assimilate the skills learned, and create their own digital mood ring.
5. Presentation: Sell your product (optional)
Personalize your product
Create a presentation to sell your unique design to your classmates
Extensions/Get Creative!
6.Completed Sample code
Sample program(s) for DIY: Mood Ring
Additional Coding Reference
Notes: This project may take as little as .5 day, or up to 1.5 days depending on student’s familiarity with both the technology and coding. Note this is NOT .5 of a class period – but .5 of a full day ~ at lease 3 hours.
This presentation is designed to be used in the classroom/camp to guide students through the tasks they will complete, teaching the coding skills they need to be familiar with.

## Slide 3: Note to the Teacher- This slide deck offers two different paths for the Classroom Presentation:
10 Minutes of Code Lessons
Slide deck is set-up for this path as the default.
“Fast Track”
Slides labelled “Fast Track” can be unhidden for an alternative approach to the 10 MOC slides.
Step-By-Step instruction on coding skills using the relevant 10 Minutes of Codes Lessons.
Students will first do 10 MOC lessons, then assimilate those skills to build the Mood Ring.
This is the recommended approach to follow for students with little to no coding experience.
Helpful for those trying to implement the project in less time.
Provides an optional path for students who may have already completed 10 Minutes of Code lessons previously, and/or have more experience with the basics of coding.
OR

## Slide 4: 1. Project Overview and Intro to Programming

## Slide 5: Mood Rings: How do they work?
Background:
The mood ring was invented by Joshua Reynolds. Mood rings enjoyed fad popularity in the 1970s and are still around today.
The stone of the ring changes color, supposedly according to the mood of the wearer.
The 'stone' of a mood ring is really a hollow glass shell containing thermotropic liquid crystals. Modern mood rings are made from a flat plastic strip containing liquid crystals that is inserted into the hollow glass and mounted within the bezel of the mood ring.
Notes: Introductory mini-project for feedback and control systems. The project includes external inputs (temperature sensor), decision logic based on the temperature sensor reading and an output (Red-Green-Blue LED).

## Slide 6: Mood Rings: How do they work?
The crystals respond to changes in temperature by twisting in a regular way. The twisting changes their molecular geometry, which alters the wavelengths of light that are reflected from the crystals.
Wavelengths of light are another way of saying color, so when the temperature of the liquid crystals change, so does the color reflected from the stone. Thus, the ring changes color with the hand temperature of the wearer.

## Slide 7: Time to DIY: Digital Mood Ring!
The Design Challenge:
Design and build a digital mood ring using the pipe cleaner that fits snugly on your finger, placement should be similar to any ring worn on the finger. Be sure the flat part of the temperature sensor is touching your skin.
In this project, you will investigate:
temperature measurement using a temperature sensor and then build a digital mood ring that changes the color of the Hub’s Red, Green, and Blue (RGB) light emitting diode (LED) as the temperature your finger changes.
You can even display what mood you are in on your calculator!
Notes: This project is an ideal introduction for students using the TI-Innovator for the first time. The “DIY- Mood Ring” project includes many of the fundamental concepts that are used in feedback and control projects. The project sets the stage for working through the more advanced Pet Car Alarm and Smart Irrigation projects.
Objectives that will be covered:
  Science Concepts: additive color model, electromagnetic spectrum (optional)
  TI-Technology Concepts: TI-Innovator™ overview, connecting TI-Innovator™ to handheld with unit-to-unit cable (connector with B label in the DATA port of the TI-Innovator), Hub menu for creating commands to send to the TI-Innovator™
  Computing Concepts: physical outputs, numeric arguments for commands

## Slide 8: Project Parts List:
TI-Nspire CX family or TI-84 Plus CE Graphing Calculator
TI-Innovator™ Hub
Temperature Sensor
Cellophane tape
Colored chenille stem (pipe cleaner)
A mood to be measured
Notes: The project works best with 2-3 students sharing Hub with Temperature sensor, and each student having their own calculator to do the programming. If equipment is limited, up to 4 students could share a Hub and temperature sensor.

## Slide 9: Engineering Design Process:
Define Problem
Design a proposed solution
Present group’s design to class.
Listen to feedback and make appropriate changes.
Build and test the design.
Use test results to make appropriate and informed changes to design.
Present your solution to class.
Notes: It might be worth it to discuss with student that in very open ended project (this project is not) all of these steps would be important. In this project, we will be on the latter half of the steps, since the problem and solution, and design is really already defined in this case.

## Slide 10: 1.2a Introduction to Programming: Ti-84 Plus CE
TI-84 Plus CE with TI-Innovator Hub
Notes: To set the context for Coding, you may want to have students review the following videos for background.
  Why Programming? Code.org video
  https://www.youtube.com/watch?v=nKIu9yen5nc&feature=youtu.be
There are several slides to review with students the important keys on the calculators as it relates to programming. There is also a “Basics of Programming” PPT that may be helpful especially students are new to the TI calculator, and/or new to programming

## Slide 11
Important Keys on your TI 84 Plus Graphing Calculator
Dangerous
Use Del Instead of Clear
Store Key
Parentheses
Notes: Whenever we need to type out commands , use the green arrows above
Be sure to close your “ ” and ( )
Select commands from the prgm menus
Programs are automatically saved as you type
Some keys take you out of the Program Editor but you don’t lose your work.
Really stress the “Use Del Instead of Clear”. If you hit clear, the entire line of code typed will be gone NOT just the character you are on.

## Slide 12: Introduction to Coding: 10 Minutes of Code!
  Unit 1: Program Basics and Displaying on the Screen
    SB 1: Using Program Editor and Syntax
    SB 2: Editing the Programs Clearing the Screen
    SB 3: Output to the Home Screen (optional)
    Application: Create a Title Screen (optional)
  Unit 3: Conditional Statements (If…)
    SB 1: Conditions and the If Statements..
    SB 2: If…then…end and compound conditions
    SB 3: If…then…else statements (optional)
  Unit 4: Repetition
    SB 1: For…Next…statements
*10 MOC for TI-84 Plus: https://education.ti.com/en/activities/ti-codes/84/10-minutes
`
TI-84
Notes: It is recommended that since this is considered an entry-level STEM Project with TI-Innovator, that students begin with 10 MOC lessons. If students are already familiar with the basics, you can skip the “ground up” approach of 10 MOC lessons, and instead, choose the “Fast Track” approach with the student tasks identified instead.
]
The Units listed are the ESSENTIAL ones (except where Optional is noted) for the skills for the Project. If time allows, you may find it to be beneficial to have students complete Unit 2 as well.
Note: Beginning programmers might find this program more accessible by using only If then statements to set temperature thresholds while some students will find if then else statements helpful.

## Slide 13: ‘Fast Track’- Student Task: Create and execute a program to display “Hello World”
Write a program that displays a text message on the calculator using the Disp command.
Extensions (Optional):
  Make your own message
  Display multiple messages
Example Code:
Disp “HELLO WORLD”
    *10 MOC for TI-84 Plus: https://education.ti.com/en/activities/ti-codes/84/10-minutes
TI-84
Notes: If student needs steps by steps support reference TI Codes: 10 Minutes of Code : Unit 1 Skill builder 1
Objectives that will be covered:
TI Technology Concepts: Introduction to TI-84 Plus CE keyboard, applications (home screen for calculations and executing programs, program editor). Intro to the Program Editor and executing programs on the home screen. Program Editor Menu I/O menu. Disp command with text string and math expression arguments.

## Slide 14: ‘Fast Track’ Student Task: Create and execute a program to display “Hello World” 10 times using a loop
Write a program that displays a text message on the calculator 10 times using For command.
Extensions (Optional):
  Try a different type of loop
TI-Nspire Example
For(I,1,10)
Disp “Hello World”
End
    *10 MOC for TI-84 Plus: https://education.ti.com/en/activities/ti-codes/84/10-minutes
TI-84
Notes: If student needs steps by steps support reference TI Codes: 10 Minutes of Code : Unit 1 Skill builder 1
Objectives that will be covered:
  TI Technology Concepts: Introduction to TI-84 Plus CE keyboard, applications (home screen for calculations and executing programs, program editor). Intro to the Program Editor and executing programs on the home screen. Program Editor Menu I/O menu. Disp command with text string and math expression arguments.

## Slide 15: Background: Programming tips
To break out of a program press and hold the ON key until you receive a Quit option.
Do not forget to be very careful with the “Clear” button – you will lose the entire line of code typed.
Use the menus as much as possible. Do not try to type out the commands
TI-84
Quit Option that occurs when you break out of a program.

## Slide 16: ‘Fast Track’ Student Task: Create and execute a program that asks how many times “Hello World” will displayed. The number of times must be between 5 and 10.
Write a program that requests a number ‘n’, determines if ‘n’ is in the correct range, and then displays the message ‘n’ times.
Extensions (Optional):
  Allow for multiple ranges and/or try a different type of loop
Disp “ENTER A NUMBER”
Prompt N
If N>5 and N<10
Then
For(I,1,N)
Disp “HELLO WORLD”
End
Else
Disp “INVALID INPUT
End
TI-84
    *10 MOC for TI-84 Plus: https://education.ti.com/en/activities/ti-codes/84/10-minutes
TI-84
Notes: If student needs steps by steps support reference TI Codes: 10 Minutes of Code : Unit 1 Skill builder 1
Objectives that will be covered:
  TI Technology Concepts: Introduction to TI-84 Plus CE keyboard, applications (home screen for calculations and executing programs, program editor). Intro to the Program Editor and executing programs on the home screen. Program Editor Menu I/O menu. Disp command with text string and math expression arguments.

## Slide 17: 2. Introduction to the tI-Innovator™ Hub

## Slide 18: Introduction to the TI-Innovator™ Hub
TI-Innovator Hub is a microcontroller controlled by the Calculator. The microcontroller inside is the MSP432 that is in many real world products.
It has a built in RED LED, COLOR LED, SPEAKER and BRIGHTNESS sensor.
It is programmed by the calculator using TI-Basic.

## Slide 19: More 10 Minutes of Code…with TI-Innovator!
If you are using the TI-84 Plus or TI-Nspire CX:
  Unit 1: Getting Started with TI-Innovator Hub
    SB 1: Your first program!
    SB 2: Input and Color
    SB 3: Request/Input and Sound (optional)
    Application: Traffic Light (optional)
  Unit 2: For Loops with TI-Innovator Hub
    SB 1: Blink the Light
    SB 2: Loop Through Colors
    SB 3: Loop through the musical notes (optional)
  *10 MOC with TI-Innovator for TI-Nspire CX: https://education.ti.com/en/activities/ti-codes/nspire/10-minutes-innovator
  *10 MOC for TI-Innovator for TI-84: https://education.ti.com/en/activities/ti-codes/84/10-minutes-innovator
Notes: It is recommended that since this is considered an entry-level STEM Project with TI-Innovator, that students begin with 10 MOC lessons. If students are already familiar with the basics, you can certainly skip this, moving on to the next slide “Fast Track” with Student Task given. .

## Slide 20: ‘Fast Track’ Student Task: Write Program to Display Colors on the TI-Innovator™ Hub
Student Task: Write Program to Display Colors
  Create and execute a program using the COLOR command to display different colors using the Red-Green-Blue LED.
Send("SET COLOR 255 0 0”)
Wait 1
Send("SET COLOR 255 0 255”)
Wait 1
Send("SET COLOR 255 127 80”)
Wait 1
Send("SET COLOR 0 0 0”)
TI-84
TI-84
Notes: If students struggle with this task, have students complete designated lessons with 10 Minutes of Code with the TI Innovator Hub : Unit 1 Skill builder 2..
COLOR (Red Green Blue) Output LEDs (Built-in the TI-Innovator™)
The COLOR object built into the TI-Innovator includes 3 LED’s that can be set together or individually. The settings are from 0, off, to 255, full power.
Note that there are 256 (2^8) states for the setting. This is referred to as an 8-bit color setting. The following slide can be used for a more-in depth discussion of the color spectrum.
Command syntax: Send(“SET COLOR red green blue”)

## Slide 21: ‘Fast Track’ Exploration: Color
What values would you enter to get blue?
What values to enter to get yellow?
Experiment with values to make your own colors
How can you make Red?
How can you make the other primary colors?
How can you make Yellow?
How can you make the other secondary colors?
How can you make White?
How can you turn off all of the colors?
Notes: Further information about the science of color perception: http://www.cyberphysics.co.uk/topics/light/colorAddition.html
There are also additional SCIENCE BACKGROUND slides in the Teacher Resource PPT if you choose to expand on the way the eyes perceive light.
COLOR (Red Green Blue) Output LEDs (Built-in the TI-Innovator™)
The COLOR object built into the TI-Innovator includes 3 LED’s that can be set together or individually. The settings are from 0, off, to 255, full power.
Note that there are 256 (2^8) states for the setting. This is referred to as an 8-bit color setting. The following slide can be used for a more-in depth discussion of the color spectrum.
Command syntax: Send(“SET COLOR red green blue”)

## Slide 22: 3. Using Input and Output devices

## Slide 23: Brightness Sensor on TI-Innovator Hub
On-Board Light Brightness Sensor is built into the TI-Innovator Hub (internal sensor). It is located at the bottom of the Hub. The sensor detects light intensity.
Readings range from 0 to 100.
Notes: You may find it helpful to talk about giving students an introduction to input vs output…Note that students will want to experiment with the light sensor… have students shine a flashlight on it, put it under something, etc. to see a range of readings from 0-100.

## Slide 24: 10 Minutes of Code with TI-Innovator: Exploring Input, Output
If you are using the TI-84 Plus or TI-Nspire CX:
  Unit 3: BRIGHTNESS, IF and WHILE with TI-Innovator Hub
    SB 1: Brightness measurements
    SB 2: Brightness & Light with IF, WHILE (optional)
    SB 3: Brightness and Color (optional)
  *10 MOC with TI-Innovator for TI-Nspire CX: https://education.ti.com/en/activities/ti-codes/nspire/10-minutes-innovator
  *10 MOC for TI-Nspire CX: https://education.ti.com/en/activities/ti-codes/nspire/10-minutes-innovator
Notes: It is recommended that since this is considered an entry-level STEM Project with TI-Innovator, that students begin with 10 MOC lessons. If students are already familiar with the basics, you can certainly skip this, moving on to the next slide “Fast Track” with Student Task given. .

## Slide 25: ‘Fast Track’: Example Code for Brightness sensor
Sample Code 84:
For A,1,20
Send("READ BRIGHTNESS”)
Get(B)
Disp B
Wait 1
End
TI-84
Student Task:
Read brightness from the sensor, and display the reading or other desired text.
Notes: This code introduces students to the While loop.

## Slide 26: Temperature Sensor
3.1 Input

## Slide 27: Connecting the Temperature Sensor
Send("CONNECT TEMPERATURE 1 TO IN 1”)
Temperature Sensor
Connects temperature sensor 1 to Input Port 1.
The numbering of the temperature sensors helps to differentiate in situations where multiple temperature sensors are connected
TI-84
Notes: Note there is no current 10 Minute of Code lesson on Using the Temperature. The sample code has been provided. Note that if students completed the lesson on brightness sensor, they will be familiar with the Read- Get-Disp- Wait command, but you will need to go over the Connect Command as it is critical.

## Slide 28: Using the Temperature Sensor
Send("CONNECT TEMPERATURE 1 TO IN 1”)
For A,1,20
Send("READ TEMPERATURE 1”)
Get(D)
Disp D
Wait 3
End
TI-84
Notes: This For loop cycles 20 times. A command is sent to the TI-Innovator to read the
value of temperature sensor 1, the Get command stores the value to variable “D”, the value of variable D is displayed, then the calculator waits for 3 seconds before going on to the End command that returns to the beginning of the loop.
Measurements
Measurement in degrees Celsius

## Slide 29: Exploration: Temperature Sensor
Are the values being displayed on the Celsius or Fahrenheit scale?
Can you insert a line of code that changes the temperature from Celsius to Fahrenheit before it is displayed?
What typical temperature values being displayed?
What is the significance of a reading of -273?
Why might the sensor read -273?
Why might you use a Wait command in your For Loop for monitoring the temperature?
Notes: Some students may want to see their readings displayed in F instead, just for ease of understanding the readings. Challenge them to insert a line of coding to do this.

## Slide 30: One line of code can change the readings from C  F:
Send("CONNECT TEMPERATURE 1 TO IN 1”)
For A,1,20
Send("READ TEMPERATURE 1”)
Get(D)
9/5*D +32 D
Disp D
Wait 3
End
TI-84
Notes: T(°F) = T(°C) × 9/5 + 32

## Slide 31: 5. Putting it all Together- DIY Mood Ring

## Slide 32: Time to DIY: Digital Mood Ring!
The Design Challenge:
Design and build a digital mood ring using the pipe cleaner that fits snugly on your finger, placement should be similar to any ring worn on the finger. Be sure the flat part of the temperature sensor is touching your skin.
In this project, you will investigate:
Temperature measurement using a temperature sensor and then build a digital mood ring that changes the color of the Hub’s Red, Green, and Blue (RGB) light emitting diode (LED) as the temperature of your finger changes.
You can even display what mood you are in on your calculator!
Notes: This project is an ideal introduction for students using the TI-Innovator for the first time. The “DIY- Mood Ring” project includes many of the fundamental concepts that are used in feedback and control projects. The project sets the stage for working through the more advanced Pet Car Alarm and Smart Irrigation projects.
Objectives that will be covered:
  Science Concepts: additive color model, electromagnetic spectrum (optional)
  TI-Technology Concepts: TI-Innovator™ overview, connecting TI-Innovator™ to handheld with unit-to-unit cable (connector with B label in the DATA port of the TI-Innovator), Hub menu for creating commands to send to the TI-Innovator™
  Computing Concepts: physical outputs, numeric arguments for commands

## Slide 33: Design Goals:
Write a program that reads and displays your skin temperature every second when the sensor is attached to your finger.
Write a program that sets at least three different colors (moods) depending on your skin temperature.

## Slide 34: Design Challenge- HINTS:
Write a program that reads and displays your skin temperature every second when the sensor is attached to your finger.
  Do this by reading the temperature in a For loop with a Wait, then use the Disp command to display the value read from the sensor.
Write a program that sets at least three different colors (moods) depending on your skin temperature.
  Use the Disp command to display the mood each temperature represents. Use If/Then statements to determine the range.
Notes: If students struggle, show this slide.

## Slide 35: Student Task: DIY Mood Ring
    Before starting to program, define the problem.
      What would be a good threshold temperature to use to turn on colors?
        What are the reasons for your choice?
        What are some ways that you can raise the temperature sensor reading?

## Slide 36: Using a flowchart to plan:
Input
Decision Point
Output
Sample, simple flowchart:
Notes: Flowcharts can be helpful tools to think through what the program needs to do.
More about using Flowcharts for planning:
https://www.codeavengers.com/notes/planning/flowcharts
draw.io is a good online tool you can use to create flowcharts. You can logon with a Google Drive account.

## Slide 37: Student Task: DIY Mood Ring
2. Develop the Solution: Write down the steps (pseudocode) before programming. Use this template:
Important steps in your program | TI-Basic commands to implement steps in your program
1. | 
2. | 
3. | 
4. | 
5… | 

## Slide 38: Student Task: HINTS
2. Develop the Solution: Write down the steps (pseudocode) before programming. Use this template:
Important steps in your program | TI-Basic commands to implement steps in your program
1. Connect your temp sensor. | 
2. Read the temperature. | 
3. If the temperature reading is below then you are sad (blue) | 
4. | 
5… | 
Notes: If students struggle with getting started, show this slide.

## Slide 39: Student Task: DIY Mood Ring
3. Write the code.
Notes: Beginning programmers might find this program more accessible by using only If then statements to set temperature thresholds while some students will find if then else statements helpful. The following slides can be used for code “reminders” as needed, but at this point, students will have learned all the snippets required.

## Slide 40: Sample Code: Decision Making and Logic Statements
If B>10
Then
Disp “B IS GREATER THAN 10”
Send("SET COLOR 0 255 0”)
End
If-Then command
If B>10
Then
Disp “B IS GREATER THAN 10”
Send("SET COLOR 255 0 0”)
Else
Disp “B LESS THAN OR EQUAL TO 10”
Send("SET COLOR 0 0 255”)
End
If-Then-Else command
If B>10 and C>100
Then
Disp “B GREATER THAN 10 AND C GREATER THAN 100”
Send("SET COLOR 0 255 0”)
End
“and”
If B>10 or C>100
Then
Disp "B GREATER THAN 10 OR C GREATER THAN 100”
Send("SET COLOR 0 255 0”)
End
“or”
Logic functions
Decision Making Commands
[2nd] test menu includes relational operators (=,>,<,etc.) and Boolean logic operators (and, not, or, etc.)
TI-84
Notes: Students will have done If/Then in Unit 3 of TI-Innovator 10 MOC, when they did the brightness sensor SB. So, the slides at this point are provided for code reminders, if students need them.

## Slide 41: Sample Code: While…loop
The While loop repeats a set of commands as long as the While condition is true.
Command Syntax:
While condition
Commands in While block
End
1B
While B>.25
Send ("READ BRIGHTNESS ”)
Get(B)
Disp B
If B>10
Then
Send("SET COLOR.GREEN ON”)
Else
Send("SET COLOR.GREEN OFF”)
End
End
Disp ”WHILE LOOP IS COMPLETE"
Note: This program uses the BRIGHTNESS sensor as a control for the While loop. If you completely cover the sensor the While loop will stop.
TI-84

## Slide 42: Extension: Get Creative!
Try these additional challenges:
  Add more than three moods.
  Add variables and logic so that the program will automatically adapt to each person’s temperature range.
  Store the temperatures values and the time to list variables. Display a plot of time vs. temperature after the For loop is done.
  Replace the For loop with a While loop.
Notes: Three moods is more complicated.

## Slide 43: 6. Presentation: Sell your Product

## Slide 44: Things to consider for your product pitch….
What makes your product unique?
How does your product work?
Why is it better than the next “mood ring” for sale?
Consider a unique name for your product, customization, etc.
Create a slogan.
Create a commercial.
Ready… set…GO! You have 5 minutes to pitch your product!
Notes: This is optional, but can really be valuable to students in working on how to present their ideas effectively to their peers. You could consider a small prize or “perk” for the winning team.

## Slide 45: 7. Completed Sample Code

## Slide 46: Example Completed Program- TI 84 Plus CE (Basic code)
Send "CONNECT TEMPERATURE 1 TO IN 1”
“Connect Temperature sensor #1 to Input port #1”
For(C,1,30)
“For loop repeats 30 times”
Send("READ TEMPERATURE 1”)
“Reads the value for Temperature sensor #1”
Get(T)
Disp T
Wait 1
“Gets to variable d then displays the value of T, then Waits 1 second”
If T<26
“Compares values of variable d to determine and show mood”
Then
Send "SET COLOR 255 0 0”
Disp ”MY MOOD IS RED”
End
If T≥26 and T<27
Then
Send "SET COLOR 0 255 0”
Disp ”MY MOOD IS GREEN”
EndIf
If T>27
Then
Send "SET COLOR 0 0 255”
Disp ”MY MOOD IS BLUE”
End
End
Send "SET COLOR 0 0 0”
“Turns the COLOR OFF”
Note: Experiment with temperature values to determine relevant temperature ranges for each person.
TI-84
This program is also available in the MoodRing_Basic.8xv file provided for your reference.

## Slide 47: TI-84 Plus CE- Sample Program (More Advanced Code)
ClrList L₁
ClrList L₂
Send("CONNECT TEMPERATURE 1 TO IN1")
For(N,1,25)
Send("READ TEMPERATURE 1")
Get(T)
Wait 1
Disp "TEMP =",T
If T≤26.6
Then
Send("SET COLOR 0 0 0")
Disp "STRESSED"
End
If T≥26.5 and T≤27
Then
Send("SET COLOR 255 0 0")
Disp "NERVOUS"
End
If T≥27 and T≤27.5
Then
Send("SET COLOR 255 140 0")
Disp "UNSETTLED"
End
If T≥27.5 and T≤28
Then
Send("SET COLOR 0 255 0")
Disp "ACTIVE"
End
If T≥28 and T≤28.5
Then
Send("SET COLOR 0 200 100")
Disp "RELAXED"
End
If T≥28.5 and T≤29
Then
Send("SET COLOR 0 255 255")
Disp "LOVABLE"
End
If T≥29 and T≤29.5
Then
Send("SET COLOR 0 0 255")
Disp "ROMANTIC"
End
If T≥29.5 and T≤30
Then
Send("SET COLOR 255 150 150)
Disp "HAPPY"
End
If T≥30 and T≤31.5
Then
Send("SET COLOR 255 128 0")
Disp "TIRED"
End
If T≥31.5 and T≤32
Then
Send("SET COLOR 255 0 128")
Disp "CALM"
End
T→L₁(1+dim(L₁))
N→L₂(1+dim(L₂))
End
This program is also available in the MoodRing_Advanced.8xv
TI-84
Notes: Students have been presented with extensions, and things to try, and there are always more than one “correct path” when it comes to coding. This is an example of more advanced code that students could generate, or you could share with students after the fact.